## Slide 1
TEMPO Mission Overview
and Status
Kelly Chance
Smithsonian Astrophysical
Observatory
tempo.si.edu
NOAA
Satellite Aerosol Product Workshop
for Science and Operational Users
September 13, 2016

## Slide 2: TEMPO summary
Currently on-schedule and on-budget
  System Requirements Review and Mission Definition Review in November 2013
  KDP-B April 2014
  Most technical issues solved at the preliminary design level, following technical interchange meeting at Ball, April 2014
  PDR on July 31, 2014
  Now in Phase C (implementation): KDP-C April 10, 2015
  Instrument CDR June 2015
  Ground Systems CDR May 2016
  Test Readiness Review August 2016
Select satellite host 2017+
  TEMPO operating longitude and launch date are not known until after host selection
Instrument delivery 08/2017 for launch 11/2018 or later, most likely in 2020 or 2021

## Slide 3: Hourly atmospheric pollution from geostationary Earth orbit
PI: Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development: Ball Aerospace
Project Management: NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, U Alabama Huntsville, U Iowa, RT Solutions, Carr Astronautics
International collaboration: Mexico, Canada, Cuba, Korea, UK,
ESA, Spain
Selected Nov. 2012 as NASA’s first Earth Venture Instrument
  NASA will arrange hosting on commercial geostationary communications satellite with launch expected NET 11/2018
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science Decadal Survey recommendations
  Makes many of the GEO-CAPE atmosphere measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team
  North American component of an international constellation for air quality observations

## Slide 4: TEMPO instrument concept
Measurement technique
  Imaging grating spectrometer measuring solar backscattered Earth radiance
  Spectral band & resolution: 290-490 + 540-740 nm @ 0.6 nm FWHM, 0.2 nm sampling
  2 2-D, 2k×1k, detectors image the full spectral range for each geospatial scene
Field of Regard (FOR) and duty cycle
  Mexico City/Yucatan, Cuba to the Canadian oil sands, Atlantic to Pacific
  Instrument slit aligned N/S and swept across the FOR in the E/W direction, producing a radiance map of Greater North America in one hour
Spatial resolution
  2.1 km N/S × 4.7 km E/W native pixel resolution (9.8 km2)
  Co-add/cloud clear as needed for specific data products
Standard data products and sampling rates
  Most sampled hourly, including eXceL O3 (troposphere, PBL)
  NO2, H2CO, C2H2O2, SO2 sampled hourly (average results for ≥ 3/day if needed)
  Nominal spatial resolution 8.4 km N/S × 4.7 km E/W at center of domain (can often measure 2.1 km N/S × 4.7 km E/W)
  Measurement requirements met up to 50o for SO2, 70o SZA for other products

## Slide 5: Baseline and threshold data products
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
Minimal set of products sufficient for constraining air quality
Across Greater North America (GNA): 18°N to 58°N near 100°W, 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months

## Slide 6: TEMPO mission concept
Geostationary orbit, operating on a commercial telecom satellite
  NASA will arrange launch and hosting services (per Earth Venture Instrument scope)
    80-115o W acceptable latitude
    Specifying satellite environment, accommodation
  Hourly measurement and telemetry duty cycle for at least ≤70o SZA
TEMPO is low risk with significant space heritage
  We proposed SCIAMACHY in 1985, as suggested by the late Dr. Dieter Perner
  All proposed TEMPO measurements have been made from low Earth orbit satellite instruments to the required precisions by SAO and Science Team members
  All TEMPO launch algorithms are implementations of currently operational algorithms
    NASA TOMS-type O3
    SO2, NO2, H2CO, C2H2O2 from fitting with AMF-weighted cross sections
    Absorbing Aerosol Index, UV aerosol, Rotational Raman scattering cloud
    SAO eXceL profile/tropospheric/PBL O3 for selected geographic targets
Example higher-level products: Near-real-time pollution/AQ indices, UV index
TEMPO research products will greatly extend science and applications
  Example research products: BrO and IO from AMF-normalized cross sections; height-resolved SO2; additional cloud/aerosol products; vegetation products; additional gases

## Slide 7: Geostationary orbit opportunities of interest
TEMPO
(typical)
Between 90 W and 110 W, there are nine owner operators of 30 satellites including older models still used in this location:
  Direct TV Group (7)
  AGS (5)
  Intelsat (5)
  Telesat (4)
  Hughes Network Systems (3)
  Echostar (2)
  SkyTerra (2)
  Inmarsat (1)
  ICO Global Communications (1)
TEMPO can be located between 80 – 120 West

## Slide 8: TEMPO hourly NO2 sweep
N.B. special operations
give 10-minute resolution
for selected longitude
regions

## Slide 9: A day in the life
Figure 7. Nominal daily operations for TEMPO instrument.

## Slide 10
Air quality requirements from the GEO-CAPE Science Traceability Matrix

## Slide 11
Ultraviolet/
visible
species
(GOME,
TEMPO,
etc.)
Infrared
species

## Slide 12: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 13: Typical TEMPO-range spectra (from SCIAMACHY, 2002-2012)

## Slide 14: LEO measurement capability
A full, minimally-redundant, set of polluting gases, plus aerosols and clouds is now measured to very high precision from satellites. Ultraviolet and visible spectroscopy of backscattered radiation provides O3 (including profiles and tropospheric O3), NO2 (for NOx), H2CO and C2H2O2 (for VOCs), SO2, H2O, O2-O2, N2 and O2 Raman scattering, and halogen oxides (BrO, ClO, IO, OClO). Satellite spectrometers we planned since 1985 began making these measurements in 1995.

## Slide 15
NO2
Vancouver
L.A.
S.F.
Seattle
Phoenix
Chicago
N.Y.
Boston
power station
Denver
Detroit
Montreal
Mexico City
Las Vegas
Dallas
Houston
Portland
Miami
Atlanta
Minneapolis

## Slide 16
NO2 - Los Angeles

## Slide 17: Los Angeles coverage
Every hour!

## Slide 18: TEMPO measurements will capture the diurnal cycle of pollutant emissions
GeoTASO NO2 Slant Column, 02 August 2014 Morning
Preliminary data,
C. Nowlan, SAO
Co-added to approx. 500m x 450m
Morning vs. Afternoon

## Slide 19: TEMPO measurements will capture the diurnal cycle of pollutant emissions
GeoTASO NO2 Slant Column, 02 August 2014 Afternoon
Preliminary data,
C. Nowlan, SAO
Co-added to approx. 500m x 450m
Morning vs. Afternoon

## Slide 20: Global pollution monitoring constellation
Sentinel-5P
(once per day)
TEMPO
(hourly)
Sentinel-4
(hourly)
GEMS
(hourly)
Courtesy Jhoon Kim,
Andreas Richter
Policy-relevant science and environmental services enabled by common observations
Improved emissions, at common confidence levels, over industrialized Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution
80-115°W
0°
2021+ launch
128.2°E
2019 launch

## Slide 21: TEMPO launch algorithms
NO2, SO2, H2CO, C2H2O2 vertical columns
  Direct fitting to TEMPO radiances
    AMF-corrected reference spectra, Ring effect, etc.
    DOAS option available to trade more speed for less accuracy, if necessary
    Research products could include H2O, BrO, OClO, IO
O3 profiles, tropospheric O3
eXceL optimal-estimation method developed @ SAO for GOME, OMI
May be extended to SO2, especially volcanic SO2
TOMS-type ozone retrieval included for heritage
Aerosol products from OMI heritage: AOD, AAOD, Aerosol Index
Advanced/improved products likely developed @ GSFC, U. Nebraska
Cloud Products from OMI heritage: CF, CTP
Advanced/improved products likely developed @ GSFC
UVB research product based on OMI heritage (FMI, GSFC)
Nighttime research products include city lights

## Slide 22
Product | Algorithm | Hourly Coverage @ ≤ 4.5×8 km2
O3 | TOMS-Vn | 15 - 50.25oN, 60 - 130oW
O3 | XL optimal estimation | Selected urban areas and burning regions
NO2 | Direct fitting, AMF (λ) | 15 - 50.25oN, 60 - 130oW
SO2 | Direct fitting, AMF (λ) | 15 - 50.25oN, 60 - 130oW
H2CO | Direct fitting, AMF (λ) | 15 - 50.25oN, 60 - 130oW
C2H2O2 | Direct fitting, AMF (λ) | 15 - 50.25oN, 60 - 130oW
Aerosol OD and SSA | AERUV | 15 - 50.25oN, 60 - 130oW
Cloud pressure and fraction | CLDRR | 15 - 50.25oN, 60 - 130oW
UBV and Eryth. dose | UVB | 15 - 50.25oN, 60 - 130oW
AQ indices | L3-L4 based | 15 - 50.25oN, 60 - 130oW
Default Launch Data Products

## Slide 23
Product | Algorithm | Hourly Coverage @ ≤ 4.5×8 km2
O3 | XL optimal estimation | 15 - 50.25oN, 60 - 130oW (or, extended regions)
BrO | Direct fitting, AMF (λ) | 15 - 50.25oN, 60 - 130oW
H2O | Direct fitting, AMF (λ) | 15 - 50.25oN, 60 - 130oW
Aerosols | AERUV+ | 15 - 50.25oN, 60 - 130oW
Clouds | CLDRR+ | 15 - 50.25oN, 60 - 130oW
SO2 | Height-resolved | 15 - 50.25oN, 60 - 130oW
Secondary and Improved Data Products

## Slide 24: www.epa.gov/rsig
TEMPO will use the EPA’s Remote Sensing Information Gateway (RSIG) for subsetting, visualization, and product distribution – to make TEMPO YOUR instrument
J. Szykman for more information

## Slide 25: AQ indices
What is an AQ index?”
“The Canadian Air Quality Health Index is a multipollutant index based on the sum of PM2.5, NO2, and O3,weighted by their contribution to mortality in daily time-series
study across Canadian cities.” [Cooper et al., 2012]
Cooper et al., for example, propose a satellite-based multipollutant index using the WHO Air Quality Guidelines (AQG):
Can we define different indices as appropriate to locations, seasons, times?
Might they be formulated using RSIG?
Might assimilation be included?
Cooper, M., R.V. Martin, A. van Donkelaar, L. Lamsal, M. Brauer, and J. Brook, A satellite-based multi-pollutant index of global air quality, Env. Sci. and Tech., 46, 8523-8524, 2012.

## Slide 26: Spectroscopic signatures
TEMPO
Visible
TEMPO
Ultraviolet
VIIRS – Day-Night Band (DNB)
Laboratory Spectra of Lighting Types (C. Elvidge): http://www.ngdc.noaa.gov/eog/night_sat/spectra.html

## Slide 27: The end! Thanks to NASA, ESA, Ball Aerospace & Technologies Corp., The Boeing Company

## Slide 28: Backups

## Slide 29: Data products, science studies (the Green Paper), special operations
Volcanic SO2 (column amount and plume altitude is a potential research product.
Diurnal out-going shortwave radiation and cloud forcing is a potential research product.
Nighttime “city lights” products, which represent anthropogenic activities at the same spatial resolution as air quality products, may be produced twice per day (late evening and early morning) as a research product. Meeting TEMPO measurement requirements for NO2 (visible) implies the sensitivity for city lights products over the CONUS within a 2-hour period at 2×4.5 km2 to 1.1×10-8 W cm-2 sr-1 μm-1.
Several additional first-measurement molecules are being studied.
H2O will be produced at launch from the 7ν vibrational polyad at 445 nm. Water vapor retrieved from the visible spectrum has good sensitivity to the planetary boundary layer, since the absorption is optically thin, and is available over both the land and ocean. The hourly coverage of TEMPO will greatly improve the knowledge of water vapor’s diurnal cycle and make rapid variations in time readily observed.

## Slide 30: Traffic, biomass burning
Morning and evening higher-frequency scans The optimized data collection scan pattern during mornings and evenings provides multiple advantages for addressing TEMPO science questions. The increased frequency of scans coincides with peaks in vehicle miles traveled on each coast.
Biomass burning The unexplained variability in ozone production from fires is of particular interest. The suite of NO2, H2CO, C2H2O2, O3, and aerosol measurements from TEMPO is well suited to investigating how the chemical processing of primary fire emissions effects the secondary formation of VOCs and ozone. For particularly important fires it is possible to command special TEMPO observations at even shorter than hourly revisit time, probably as short as 10 minutes.

## Slide 31: NOx studies
Lightning NOx Interpretation of satellite measurements of tropospheric NO2 and O3, and upper tropospheric HNO3 lead to an overall estimate of 6 ± 2 Tg N y-1 from lightning [Martin et al., 2007]. TEMPO measurements, including tropospheric NO2 and O3, can be made for time periods and longitudinal bands selected to coincide with large thunderstorm activity, including outflow regions, with fairly short notice.
Soil NOx Jaeglé et al. [2005] estimate 2.5 - 4.5 TgN y-1 are emitted globally from nitrogen-fertilized soils, still highly uncertain. The US a posteriori estimate for 2000 is 0.86 ± 1.7 TgN y-1. For Central America it is 1.5 ± 1.6 TgN y-1. They note an underestimate of NO release by nitrogen-fertilized croplands as well as an underestimate of rain-induced emissions from semiarid soils.
TEMPO is able to follow the temporal evolution of emissions from croplands after fertilizer application and from rain-induced emissions from semi-arid soils. Higher than hourly time resolution over selected regions may be accomplished by special observations. Improved constraints on soil NOx emissions may also improve estimated of lightning NOx emissions [Martin et al. 2000].

## Slide 32: Halogens
BrO will be produced at launch, assuming stratospheric AMFs. Scientific studies will correct retrievals for tropospheric content. IO was first measured from by SAO space using SCIAMACHY spectra [Saiz-Lopez et al., 2007]. It will be produced as a scientific product, particularly for coastal studies, assuming AMFs appropriate to lower tropospheric loading.
The atmospheric chemistry of halogen oxides over the ocean, and in particular in coastal regions, can play important roles in ozone destruction, oxidizing capacity, and dimethylsulfide oxidation to form cloud-condensation nuclei [Saiz-Lopez and von Glasow, 2012]. The budgets and distribution of reactive halogens along the coastal areas of North America are poorly known. Therefore, providing a measure of the budgets and diurnal evolution of coastal halogen oxides is necessary to understand their role in atmospheric photochemistry of coastal regions. Previous ground-based observations have shown enhanced levels (at a few pptv) of halogen oxides over coastal locations with respect to their background concentrations over the remote marine boundary layer [Simpson et al., 2015]. Previous global satellite instruments lacked the sensitivity and spatial resolution to detect the presence of active halogen chemistry over mid-latitude coastal areas. TEMPO observations together with atmospheric models will allow examination of the processes linking ocean halogen emissions and their potential impact on the oxidizing capacity of coastal environments of North America.
TEMPO also performs hourly measurements one of the world’s largest salt lakes: the Great Salt Lake in Utah. Measurements over Salt Lake City show the highest concentrations of BrO over the globe. Hourly measurement at a high spatial resolution can improve understanding of BrO production in salt lakes.

## Slide 33: Spectral indicators
Fluorescence and other spectral indicators Solar-induced fluorescence (SIF) from chlorophyll over both land and ocean will be measured. In terrestrial vegetation, chlorophyll fluorescence is emitted at red to far-red wavelengths (~650-800 nm) with two broad peaks near 685 and 740 nm, known as the red and far-red emission features. Oceanic SIF is emitted exclusively in the red feature. SIF measurements have been used for studies of tropical dynamics, primary productivity, the length of carbon uptake period, and drought responses, while ocean measurements have been used to detect red tides and to conduct studies on the physiology, phenology, and productivity of phytoplankton. TEMPO can retrieve both red and far-red SIF by utilizing the property that SIF fills in solar Fraunhofer and atmospheric absorption lines in backscattered spectra normalized by a reference (e.g., the solar spectrum) that does not contain SIF.
TEMPO will also be capable of measuring spectral indices developed for estimating foliage pigment contents and concentrations. Spectral approaches for estimating pigment contents apply generally to leaves and not the full canopy. A single spectrally invariant parameter, the Directional Area Scattering Factor (DASF), relates canopy-measured spectral indices to pigment concentrations at the leaf scale.
UVB TEMPO measurements of daily UV exposures build upon heritage from OMI and TROPOMI measurements. Hourly cloud measurements from TEMPO allow taking into account diurnal cloud variability, which has not been previously possible. The OMI UV algorithm is based on the TOMS UV algorithm. The specific product is the downward spectral irradiance at the ground (in W m-2 nm-1) and the erythemally weighted irradiance (in W m-2).

## Slide 34: Air quality and health
TEMPO’s hourly measurements allow better understanding of the complex chemistry and dynamics that drive air quality on short timescales. The density of TEMPO data is ideally suited for data assimilation into chemical models for both air quality forecasting and for better constraints on emissions that lead to air quality exceedances. Planning is underway to combine TEMPO with regional air quality models to improve EPA air quality indices and to directly supply the public with near real time pollution reports and forecasts through website and mobile applications. As a case study, an OSSE for the Intermountain West was performed to explore the potential of geostationary ozone measurements from TEMPO to improve monitoring of ozone exceedances and the role of background ozone in causing these exceedances (Zoogman et al. 2014).

## Slide 35: Clouds and aerosols
Clouds The launch cloud algorithm is be based on the rotational Raman scattering (RRS) cloud algorithm that was developed for OMI by GSFC. Retrieved cloud pressures from OMCLDRR are not at the geometrical center of the cloud, but rather at the optical centroid pressure (OCP) of the cloud. Additional cloud products are possible using the O2-O2 collision complex and/or the O2 B band.
Aerosols TEMPO’s launch algorithm for retrieving aerosols will be based upon the OMI aerosol algorithm that uses the sensitivity of near-UV observations to particle absorption to retrieve Absorbing Aerosol Index (AAI), aerosol optical depth (AOD) and single scattering albedo (SSA). TEMPO may be used together with the advanced baseline imager (ABI) instruments on the NOAA GOES-R and GOES-S satellites for aerosol retrievals, reducing AOD and fine mode AOD uncertainties from 30% to 10% and from 40% to 20%.

## Slide 36
Team Member | Institution | Role | Responsibility
K. Chance | SAO | PI | Overall science development; Level 1b, H2CO, C2H2O2
X. Liu | SAO | Deputy PI | Science development, data processing; O3 profile, tropospheric O3
J. Al-Saadi | LaRC | Deputy PS | Project science development
J. Carr | Carr Astronautics | Co-I | INR Modeling and algorithm
M. Chin | GSFC | Co-I | Aerosol science
R. Cohen | U.C. Berkeley | Co-I | NO2 validation, atmospheric chemistry modeling, process studies
D. Edwards | NCAR | Co-I | VOC science, synergy with carbon monoxide measurements
J. Fishman | St. Louis U. | Co-I | AQ impact on agriculture and the biosphere
D. Flittner | LaRC | Project Scientist | Overall project development; STM; instrument cal./char.
J. Herman | UMBC | Co-I | Validation (PANDORA measurements)
D. Jacob | Harvard | Co-I | Science requirements, atmospheric modeling, process studies
S. Janz | GSFC | Co-I | Instrument calibration and characterization
J. Joiner | GSFC | Co-I | Cloud, total O3, TOA shortwave flux research product
N. Krotkov | GSFC | Co-I | NO2, SO2, UVB
M. Newchurch | U. Alabama Huntsville | Co-I | Validation (O3 sondes, O3 lidar)
R.B. Pierce | NOAA/NESDIS | Co-I | AQ modeling, data assimilation
R. Spurr | RT Solutions, Inc. | Co-I | Radiative transfer modeling for algorithm development
R. Suleiman | SAO | Co-I, Data Mgr. | Managing science data processing, BrO, H2O, and L3 products
J. Szykman | EPA | Co-I | AIRNow AQI development, validation (PANDORA measurements)
O. Torres | GSFC | Co-I | UV aerosol product, AI
J. Wang | U. Nebraska | Co-I | Synergy w/GOES-R ABI, aerosol research products
J. Leitch | Ball Aerospace | Collaborator | Aircraft validation, instrument calibration and characterization
D. Neil | LaRC | Collaborator | GEO-CAPE mission design team member
TEMPO Science Team, U.S.

## Slide 37
Team Member | Institution | Role | Responsibility
Randall Martin | Dalhousie U. | Collaborator | Atmospheric modeling, air mass factors, AQI development
Chris McLinden | Environment Canada | Collaborator | Canadian air quality coordination
Michel Grutter de la Mora | UNAM, Mexico | Collaborator | Mexican air quality coordination
Gabriel Vazquez | UNAM, Mexico | Collaborator | Mexican air quality, algorithm physics
Amparo Martinez | INECC, Mexico | Collaborator | Mexican environmental pollution and health
J. Victor Hugo Paramo Figeuroa | INECC, Mexico | Collaborator | Mexican environmental pollution and health
Brian Kerridge | Rutherford Appleton Laboratory, UK | Collaborator | Ozone profiling studies, algorithm development
Paul Palmer | Edinburgh U., UK | Collaborator | Atmospheric modeling, process studies
Alfonso Saiz-Lopez | CSIC, Spain | Collaborator | Atmospheric modeling, process studies
Juan Carlos Antuña Marrero | GOAC, Cuba | Collaborator | Cuban Science team lead, Cuban air quality
Osvaldo Cuesta | GOAC, Cuba | Collaborator | TEMPO validation, Cuban air quality
René Estevan Arredondo | GOAC, Cuba | Collaborator | TEMPO validation, Cuban air quality
J. Kim | Yonsei U. | Collaborators, Science Advisory Panel | Korean GEMS, CEOS constellation of GEO pollution monitoring
C.T. McElroy | York U. Canada |  | CSA PHEOS, CEOS constellation of GEO pollution monitoring
B. Veihelmann | ESA |  | ESA Sentinel-4, CEOS constellation of GEO pollution monitoring
J.P. Veefkind | KNMI |  | ESA Sentinel-5P (TROPOMI)
TEMPO Science Team, non-U.S.

## Slide 38: TEMPO footprint (GEO at 100º W)
For GEO at 80ºW, pixel size at 36.5ºN, 100ºW is 2.2 km × 5.2 km.
Location | N/S (km) | E/W (km) | GSA (km2)
36.5oN, 100oW | 2.11 | 4.65 | 9.8
Washington, DC | 2.37 | 5.36 | 11.9
Seattle | 2.99 | 5.46 | 14.9
Los Angeles | 2.09 | 5.04 | 10.2
Boston | 2.71 | 5.90 | 14.1
Miami | 1.83 | 5.04 | 9.0
Mexico City | 1.65 | 4.54 | 7.5
Canadian oil sands | 3.94 | 5.05 | 19.2
Assumes 2000 N/S pixels |  |  | 

## Slide 39: Low Earth orbit: Sun-synchronous nadir heritage
Instrument | Detectors | Spectral Coverage [nm] | Spectral Res. [nm] | Ground Pixel Size [km2] | Global Coverage
GOME-1 (1995-2011)‏ | Linear Arrays | 240-790 | 0.2-0.4 | 40×320 (40×80 zoom) | 3 days
SCIAMACHY (2002-2012)‏ | Linear Arrays | 240-2380 | 0.2-1.5 | 30×30/60/90 30×120/240 | 6 days
OMI (2004)‏ | 2-D CCD | 270-500 | 0.42-0.63 | 13×24 - 42×162 | daily
GOME-2a,b (2006, 2012) | Linear Arrays | 240-790 | 0.24-0.53 | 40×80 (40×10 zoom) | near-daily
OMPS-1 (2011) | 2-D CCDs | 250-380 | 0.42-1.0 | 50×50 | daily
Previous experience (since 1985 at SAO and MPI)
Scientific and operational measurements of pollutants O3, NO2, SO2, H2CO, C2H2O2 (& CO, CH4, BrO, OClO, ClO, IO, H2O, O2-O2, Raman, aerosol, ….)

## Slide 40: XL ozone profile retrievals
Retrieval averaging kernels based on iterative nonlinear retrievals from synthetic TEMPO radiances with the signal to noise ratio (SNR) estimated using the TEMPO SNR model at instrument critical design review in June 2015 for (a) UV (290-345 nm) retrievals and (b) UV/Visible (290-345 nm, 540-650 nm) retrievals for clear-sky condition and vegetation surface with solar zenith angle 25°, viewing zenith angle 45° and relative azimuthal angle 86°. DFS is degrees of freedom for signal, the trace of the averaging kernel matrix, which is an indicator of the number of pieces of independent information in the solution.

## Slide 41: TEMPO science questions
What are the temporal and spatial variations of emissions of gases and aerosols important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How can observations from space improve air quality forecasts and assessments for societal benefit?
How does intercontinental transport affect air quality?
How do episodic events, such as wild fires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?

## Slide 43: TEMPO template