## Slide 1: eIDEA: NOAA’s New Website for Fire and Smoke Products
Amy K. Huff (Penn State University)
Shobha Kondragunta (NOAA)
Hai Zhang (IMSG at NOAA)

## Slide 2: eIDEA: Like IDEA, but Simpler
Several requests from AQPG user group to have separate section/tab on IDEA to show only current info – make IDEA “simpler”
Around same time, NOAA launched Blended Fire and Smoke Initiative (began May 2014)
Objectives:
  Evaluate the current use of geostationary and polar-orbiting satellite capabilities in support of the Fire and Smoke mission
  Identify current SNPP/JPSS and new GOES-R data and capabilities with the potential to improve support to this mission
  Establish methodologies and procedures for the operational demonstrations of these capabilities
  Identify the satellite capabilities whose operational impacts are sufficient to warrant transition from research to operations
Result is eIDEA (“enhanced” IDEA)

## Slide 3: Enhanced Infusing satellite Data into Environmental Applications
http://www.star.nesdis.noaa.gov/smcd/spb/aq/eidea/
main product overlay buttons
animations and external links

## Slide 4: eIDEA Uses Data from the VIIRS Instrument on SNPP Satellite
SNPP launched Oct 28, 2011
VIIRS has 22 spectral bands with high spatial resolution (up to 750 m)
Afternoon overpass time, so observations made ~1:30 PM local time (1 day temporal resolution)
  So “today’s” near-real time VIIRS observations on eIDEA are available in the mid-afternoon, typically ~2-3 hours after overpass
  Archived VIIRS products in eIDEA begin on Feb 29, 2016

## Slide 5: Fire and Smoke Products on eIDEA
Overlays:
  VIIRS aerosol optical thickness (AOT)
  VIIRS smoke mask
  VIIRS fire hotspots and fire radiative power (RFP)
  VIIRS estimated surface fine particulate matter (PM2.5) concentration
  VIIRS true color imagery (RGB)
  Ambient surface PM2.5 concentrations (from U.S. EPA’s AirNow network)
Animations:
  48-hour aerosol forward trajectories
  3-day movies (AOT, smoke mask, and PM2.5)

## Slide 6: Aerosol Optical Thickness (AOT)
Aerosol optical thickness (AOT) is a measure of the scattering and absorption of visible light by aerosols (particles) in the atmosphere
AOT is also called aerosol optical depth (AOD)
Challenge for satellite instruments is to distinguish aerosols from clouds in atmosphere and from bright surfaces (e.g., cities, mountains)
AOT algorithm used to calculate AOT from satellite instrument measurements at various wavelengths
  Algorithm compares measurements from wavelengths in the visible and near-IR to find contribution from aerosols versus clouds and surface reflectance
  For example, most aerosols do not absorb/scatter around 2.1 μm (near-IR), so this wavelength can be used to obtain the contribution of the surface reflectance
  Other infrared channels are used to detect clouds
Usually different AOT algorithms for land and ocean

## Slide 7: VIIRS Aerosol Optical Thickness (AOT)
AOT indicates the presence of aerosols, like smoke, in the atmosphere
AOT is unitless; values typically range from 0 to 1 in the U.S.
Higher values of AOT (red, orange, yellow colors) correspond to higher amounts of aerosols
Clouds block the measurement of AOT, so there is no AOT in white cloud-covered areas
Example: smoke in Midwest, Aug 29, 2015
AOT Scale (no units)

## Slide 8: VIIRS Smoke Mask
The smoke mask is a qualitative indicator of smoke
Use the smoke mask to identify local and transported smoke plumes
Smoke mask derived using spectral and spatial threshold tests based on VIIRS measurements in visible and IR
Colored in shades of pink:
  Light pink: thin smoke
  Bright pink: thick smoke
  Scale at top of image
Example: smoke from fires in Pacific NW, Aug 24, 2015
Smoke Mask Scale

## Slide 9: VIIRS Fire Hotspots (Fire Detections)
Red-colored fire hotspots indicate the location of fires sensed by VIIRS
Quantitative measure of fire intensity given by fire radiative power (FRP) in units of MW
Size of red dots indicates magnitude of FRP:
  Larger the dot, the more intense the fire
  Scale at top of image
Example: fires in Pacific NW, Aug 24, 2015
Fire Radiative Power (FRP) scale (in MW)

## Slide 10: VIIRS AOT-Derived Surface PM2.5
PM2.5 is a criteria air pollutant; general name for small aerosols (diameter ≤2.5 mm) in the atmosphere, including smoke
AOT can be used to estimate surface PM2.5 concentrations; provides idea of health risk of smoke
Color coded scale (mg/m3)
  Green/yellow: low PM2.5
  Orange/red: high PM2.5
Example: smoke in Pacific NW, Aug 19, 2015
PM2.5 scale (in mg/m3)

## Slide 11: VIIRS Satellite Data are Not Surface Measurements
It is very important to remember that VIIRS aerosol products are measurements in a column of the atmosphere
VIIRS does not measure smoke or AOT directly at the surface
Sometimes VIIRS will indicate areas of smoke that are aloft in the atmosphere
To know if the smoke is reaching the surface, look at ambient PM2.5 concentrations (next slide)
  High ambient PM2.5 indicates smoke mixing to surface

## Slide 12: Overlay of Ambient PM2.5 Concentration Measurements from AirNow Network
Ambient PM2.5 from U.S. EPA’s AirNow network available as an overly of colored dots
Same color coded scale (mg/m3) as for estimated PM2.5 from VIIRS
High ambient PM2.5 tells you smoke is reaching surface
Example: smoke in Pacific NW, Aug 19, 2015, reaching surface in WA, ID, OR (red/orange dots)
PM2.5 scale (in mg/m3)

## Slide 13: True Color Imagery (RGB)
True color image looks like a picture but it is made from combining the red, green, and blue bands of VIIRS (abbreviated RGB)
  Clouds are white
  Forests/fields are green
  Mountains/deserts are brown
  Oceans/lakes are blue
  Smoke is grey
Example: smoke in Midwest, Aug 29, 2015
smoke

## Slide 14: VIIRS AOT and True Color Imagery Complement Each Other
VIIRS True Color Imagery showing smoke from fires (and red fire hotspots)
VIIRS AOD high AOD corresponds to smoke
Carlton Complex Fires in Washington State, Aug 10, 2014

## Slide 15: 48-Hour Forward Aerosol Trajectories
Trajectories give idea of transport of aerosol plumes
Areas of high AOT (>0.4) used as starting locations
Trajectories initialized at 50, 100, 150, and 200 mb above surface
  Trajectories run using NAM 12Z run output:
    Pink: near surface
    White: away from surface
  850 mb wind vectors (white)
  3-hr accumulated precipitation (yellow)

## Slide 16: eIDEA: Overlays
“Smoke Mask” is default smoke product; click on “AOT” or “Satellite Derived PM2.5” to switch b/w smoke products
Slider bars adjust opacity of RGB and smoke products
Add/remove additional product overlays using toggle buttons
Click “Save Image” to save configuration as a graphics file
Product legends

## Slide 17: Anomaly in Smoke Mask Display
May notice “missing” smoke mask data in locations where VIIRS swaths overlap (such as central US)
Caused by two issues:
  Algorithm issue
    Smoke mask algorithm behaves differently for different solar- satellite viewing geometries
  Display issue
    RGB only displays the last overpass
    Smoke mask displays both (overlapping) overpasses
    May see inconsistency between smoke mask and RGB, such as smoke over clouds, shift of smoke mask, etc.
Aerosol team working to resolve this anomaly

## Slide 18: Example for August 21, 2015: RGB Imagery
Overpass 1 (1840 UTC)
Overpass 2 (2020 UTC)
eIDEA only plots the RGB image from Overpass 2 for the overlapping region

## Slide 19: Example for August 21, 2015: Smoke Mask
Overpass 1 (1840 UTC)
Overpass 2 (2020 UTC)
Because of different solar/satellite geometries, the smoke mask algorithm obtains different results
In this case, Overpass 2 detected much less smoke
Plot Overpass 1 if nothing detected in Overpass 2 for overlapping region to increase data coverage

## Slide 20: eIDEA: Animations
Click to view animations
Links to NOAA Hazard Mapping System (HMS), main IDEA, and eIDEA-Alaska webpages
Link to additional documentation
Animation controls
Product legends
Product Description
Click “Home” or eIDEA logo to return to home page

## Slide 21: 3-Day Movie Loops
Animation controls
AOT
Regional subsets
Smoke Mask and RFP
PM2.5

## Slide 22: Navigation Tools
Click on date to open calendar
Click on specific date to select it
“Today” is shaded yellow
Use arrow buttons in calendar to change month
Use arrows on either side of selected date to load data for previous or next day
Use + or – buttons to zoom in/out
Or double click on map to zoom in
Or scroll forward/backward

## Slide 23: Visualization Tools
Click on “County” button to turn county boundaries on/off
Click on “Labels” button to turn local, state, and national labels and boundaries on/off

## Slide 24: Next Steps for eIDEA
We demonstrated eIDEA to NWS Incident Meteorologists (IMETs) in March 2016
  We already used their initial feedback to improve eIDEA
  Expecting additional feedback after the 2016 fire season
We will use your feedback from today to improve eIDEA as well! (group discussion)
Working toward additional formats for fire and smoke products:
  Mobile app coming in next year
  AWIPS-II coming soon
GOES-R data coming next year!!!

## Slide 25: Breakout Session
Please break into groups of 2-3; at least one group member must have a laptop
Focus on a few days this summer when smoke impacted your region or forecast area
Open the eIDEA website: http://www.star.nesdis.noaa.gov/smcd/spb/aq/eidea
Use the “Case Study Worksheet” to guide your analysis
Answer questions on the “Case Study Questionnaire” – we will use it to guide our discussion before lunch (and I’ll collect it so we can capture your feedback)