## Slide 1: Navy Aerosol and Visibility Forecasting: Use of Satellite Aerosol Data
  Edward Hyer
NRL – Monterey, CA
NOAA Satellite Aerosol Workshop – College Park, MD
14 September 2016

## Slide 2: In This Talk
Navy Aerosol Forecasting: Motivation
Satellite Data in the Forecasting System
Specific product needs for data assimilation
Satellite data pre-processing for assimilation
Results with VIIRS IDPS Aerosol product
Results with VIIRS Enterprise Aerosol product
Next Steps

## Slide 3: Navy Aerosol Prediction - Motivation
Can you tell us when this is coming?
How long until we can see again?
Visibility Impacts: Optical Atmosphere
Physical Impacts: e.g. dust/ash in jet engines
Health impacts
26 October 2007
Channel Islands Air National Guard Base
18 July 2009
Phoenix Sky Harbor Intl. Airport

## Slide 4: Satellite Data in Navy Aerosol Applications
Component Assimilated Data
FLAMBE – Hourly, global, biomass emission fluxes in real-time and archived since 2000
DSD – Global dust source database
NAVDAS-AOD – data assimilation, produces 6-hourly, global 3-d distributions of aerosol species (sulfate, smoke, dust, salt), in real-time and back to 2000
NAAPS Validation
MODIS and GOES data used to produce gridded smoke emissions (FLAMBE, WF-ABBA)
R&D: Himawari-8 (GOES-R to come)
MODIS Dust Enhancement Product, NRL DEBRA product from Meteosat, and TOMS AI used to identify dust sources
NRL Level 3 version of MODIS AOD
--+VIIRS AOD +AVHRR AOD
AERONET and CALIPSO climatology used for speciation
R&D: CALIPSO used for 3-d var data assimilation and validation , GEO AOD under testing
AERONET – AOD, absorption, size
CALIPSO and MISR – Vertical Profile

## Slide 5: The Navy Aerosol Analysis and Prediction System (NAAPS)
Operational since 2005 (first global operational forecast in the world)
Satellite AOD assimilation operational since 2009 (world’s first)
  In 2013, NAAPS was upgraded from 1-degree to 1/3-degree resolution
    Also upgraded from NOGAPS to NAVGEM meteorology
  Model details in Lynch et al. GMD 2016

## Slide 6: AOD Data Assimilation for NAAPS
Navy Aerosol Analysis and Prediction System (NAAPS) operational since 2005
Navy Variational Data Assimilation System for AOD (NAVDAS-AOD) Operational at FNMOC from September 2009 (MODIS over ocean)
Global MODIS is assimilated operationally as of February 2012
J.L. Zhang et al., “A System for Operational Aerosol Optical Depth Data Assimilation over Global Oceans”, JGR 2008.
MODIS AOD
MODIS RGB
NAAPS “Prior”
NAAPS + NAVDAS

## Slide 7: Preparation of Satellite AOD for Assimilation
We start with Level 2 products generated by upstream data centers

## Slide 8: Preparation of Satellite AOD for Assimilation
Post-process developed by NRL and UND, includes
Aggressive cloud filtering
Ocean wind speed correction
Land albedo correction
land surface and snow filters
Microphysical AOD bias correction
Aggregation for noise reduction
Estimation of prognostic uncertainty

## Slide 9: NRL’s process for QA/QC of new satellite AOD products: 5 stages
  Starting with a multi-month record of L2 data…
  L2/L2 comparison to AERONET at full resolution
  L2/L2 comparison to MODIS
    Generation of candidate L3 AOD…
  L3/L3 comparison to currently assimilated datasets
    Test runs of NAAPS+NAVDAS-AOD using new data…
  Model/Model comparison of analyzed aerosol fields
  Model/AERONET comparison and model verification

## Slide 10: Aerosol Data Products – Lots of Them!
Polar
  MODIS
    Dark Target
      Levy et al., AMT 2013
    Deep Blue
      Sayer et al., JGR 2013
    MAIAC
      Lyapustin et al., JGR 2011
  VIIRS
    IDPS
      (Jackson et al., JGR 2013)
      (Liu et al., JGR 2014)
    MODIS-like
      Levy et al., AMT 2015
    NOAA NDA-Enterprise
      Liu et al. JGR 2016
      More on this later!
  And many more!
Geostationary
  GOES
    GASP
      Prados et al., JGR 2007
  Korea COMS
    Meteorological Imager
      Mijin et al., RSE 2013
    Global Ocean Color Imager
      Lee et al., RSE 2010
      Myungje Choi et al., AMTD
  Himawari-8
  And many more!
Nighttime AOD retrieval
  VIIRS DNB: McHardy et al. AMT 2015

## Slide 11: Aerosol Data Products – Lots of Them!
Polar
  MODIS
    Dark Target
      Levy et al., AMT 2013
    Deep Blue
      Sayer et al., JGR 2013
    MAIAC
      Lyapustin et al., JGR 2011
  VIIRS
    IDPS
      (Jackson et al., JGR 2013)
      (Liu et al., JGR 2014)
    MODIS-like
      Levy et al., AMT 2015
    NOAA NDA-Enterprise
      Liu et al. JGR 2016
      More on this later!
  And many more!
Geostationary
  GOES
    GASP
      Prados et al., JGR 2007
  Korea COMS
    Meteorological Imager
      Mijin et al., RSE 2013
    Global Ocean Color Imager
      Lee et al., RSE 2010
      Myungje Choi et al., AMTD
  Himawari-8
  And many more!
Nighttime AOD retrieval
  VIIRS DNB: McHardy et al. AMT 2015
We cannot hope to transition all of these products to our operational data assimilation system!
Is there some way we can predict the forecast impact of each new product?

## Slide 12: Forecast Data Impact Study: Zhang et al., JGR 2014
Ocean-only, Terra only
Land+OceanTerra+Aqua
RMSE
NAAPS vs AERONET
Forecast Length (hours)

## Slide 13: More Data, Better Forecast: Some Follow-up Questions
Why does forecast improvement not scale with data volume?
Why does the forecast skill not degrade smoothly?
Can we predict the impact of added observations?
More Coverage!
(+DB+MISR)

## Slide 14: Using Time-Since-Last-Observation gives linear impact of additional data
Using Terra+Aqua buys nearly 12 hours improvement in T-S-L-O
Terra+Aqua forecast errors fall very close to estimate based on Aqua only

## Slide 15: VIIRS Enterprise AOD can add very high observation volume
Fraction of Days with Assimilation Data (May-June-July 2015)
NRL/UND MODIS Level 3
VIIRS NDA ‘FullQA’
Comparison for May-June-July 2015
MODIS Collection 5 processed to NRL/UND L3 Data Assimilation Product
VIIRS Enterprise AOD processed using in-granule QA + Textural Filtering

## Slide 16: NOAA Enterprise AOD vs IDPS VIIRS Aerosol EDR
3-month comparison to MODIS NRL/UND L3 Data Assimilation product: 201505-201507
VIIRS data aggregated and filtered ‘FullQA’ + buddy checks and neighborhood tests
Left: map of AOD differences (paired) (smoothed for plotting)
Right: scatter-density plot of AOD differences vs MODIS
IDPS
Mean AOD difference (VIIRS-MODIS)
1
2
3

## Slide 17: NOAA Enterprise AOD vs IDPS VIIRS Aerosol EDR
VIIRS data aggregated and filtered ‘FullQA’ + buddy checks and neighborhood tests
3-month comparison to MODIS NRL/UND L3 Data Assimilation product: 201505-201507
  Left: map of AOD differences (paired) (smoothed for plotting)
  Right: scatter-density plot of AOD differences vs MODIS
    Reduced bias over open ocean
    Reduced bias over land
    Inclusions of high AOD values (excluded from IDPS product)
Data assimilation testing of new Enterprise product is underway at NRL
Enterprise
Mean AOD difference (VIIRS-MODIS)
1
2
3

## Slide 18: VIIRS Enterprise Product shows good agreement with AERONET
Comparison for May-June-July 2015
Gridded comparisons to global AERONET L2.0
See Liu et al. JGR 2016 for L2 detailed comparisons to AERONET
NRL/UND MODIS Level 3
VIIRS NDA ‘FullQA’

## Slide 19: Conclusions
Navy aerosol applications require high-quality datasets in near-real-time
Aerosol forecasts are data-limited: additional high-quality data needed to maximize forecast skill
VIIRS Enterprise AOD product is a high-quality AOD dataset
    Compares well with NRL/UND L3 MODIS currently assimilated
    Compares well with ‘gold standard’ AERONET AOD
  NRL is currently testing forecast impact of NOAA Enterprise AOD product

## Slide 20: Thank You!
NRL:
    Jeff Reid
    Doug Westphal
    Peng Lynch
    Arunas Kuciauskas
U. North Dakota:
    Jianglong Zhang
    Yingxi Shi
      (now at NASA-GSFC)
    Ted McHardy
Sponsors:

## Slide 21: Extra Slides

## Slide 22: We know the location and time of all our assimilated observations
MODIS orbit (sunlit node only) dictates patterns of data availability

## Slide 23: We know the location and time of all our verification data
These spatial differences will affect the distribution of AODs used for verification (land vs. ocean, polluted vs clean)

## Slide 24: Prognostic Error Model: MODIS vs Enterprise VIIRS
Satellite Retrieved AOD (Prognostic)

## Slide 25: VIIRS Enterprise “OCEAN” vs MODIS L3

## Slide 26: VIIRS Enterprise “LAND-SW” vs MODIS L3

## Slide 27: VIIRS Enterprise “LAND-SWIR” vs MODIS L3

## Slide 28: VIIRS Enterprise “LAND-BRIGHT” vs MODIS L3

## Slide 29: VIIRS Enterprise vs MODIS: Smoke Box

## Slide 30: VIIRS Enterprise vs MODIS: Dust Box

## Slide 31: VIIRS Enterprise vs MODIS: Boreal Fire Smoke