## Slide 1: Enterprise Processing System (EPS) Aerosol Detection Product
Shobha Kondragunta and Istvan Laszlo
NOAA/NESDIS Center for Satellite Applications and Research
Pubu Ciren
IMSG

## Slide 2: Aerosol Detection Product
Identify the presence of aerosol in the atmosphere and classify it as dust or smoke or volcanic ash.
  Required accuracy: 80% for dust; 70% for smoke; 60% for volcanic ash
  Attributes:
  Qualitative imagery product
Useful applications: operational air quality forecasting; aerosol data assimilation in numerical models
SNPP VIIRS RedGreenBlue Image
 | GOES-R ABI | SNPP VIIRS
Spatial | 2 km | 750 m
Temporal | 5 min | Once a day
Coverage | Regional | Global

## Slide 3: Enterprise Processing System Approach
ABI
AHI
SNPP
Aqua
Sensors with different bands, resolution, pixel size, geographical coverage, and frequency but one scientific algorithm and software to process the data and generate aerosol product outputs in same format.
TEMPO

## Slide 4
No
Allocate RAM & read input
Start
End
Output
results
Initialize output
Process each pixel
Land?
Daytime?
Clouds, snow/ice and turbid water screening over ocean
Update output for current pixel
IR-Visible
Smoke
detection
IR-Visible
Dust
detection
No
Yes
Done
Allocate RAM & read input
Start
End
Output
results
Initialize output
Process each pixel
Land?
Daytime?
Update output for current pixel
Deep-blue
Smoke
detection
No
No
Yes
Allocate RAM & read input
Start
End
Output
results
Clouds and snow/ice screening
over land
Initialize output
Process each pixel
Land?
Daytime?
IR-Visible
Smoke
detection
Deep-blue
Dust
detection
Update output for current pixel
Deep-blue
detection
Yes
No
Yes
Yes
Yes
Algorithm path
IR-Visible
Dust
detection
Deep-blue
Smoke
detection
Algorithm path
No
1
3
2
1
2
3
EPS Aerosol Detection

## Slide 5
EPS Algorithm |  | Sensor |  |  | 
 |  | VIIRS | MODIS | ABI | AHI
1 | 0.412µm | M1 | Band 8 | X | X
2 | 0.445 µm | M2 | Band 9 | X | X
3 | 0.488 µm | M3 | Band 3 | Band 1 | Band1
4 | 0.555 µm | M4 | Band 4 | X | x
5 | 0.640 µm | M5 | Band 1 | Band 2 | Band3
6 | 0.746 µm | M6 | Band 15 | X | X
7 | 0.865 µm | M7 | Band 2 | Band 3 | Band 4
8 | 1.24 µm | M8 | Band 5 | X | X
9 | 1.38 µm | M9 | Band 26 | Band 4 | X (Band 5)*
10 | 1.61 µm | M10 | Band 6 | Band 5 | Band 5
11 | 2.25 µm | M11 | Band 7 | Band 6 | Band 6
12 | 3.70 µm | M12 | Band 20 | X(Band 7)* | X(Band 7)*
13 | 4.05 µm | M13 | Band 21 | Band 7 | Band 7
15 | 10.7 µm | M15 | Band 31 | Band 14 | Band 14
15 | 12.01 µm | M16 | Band 32 | Band 15 | Band 15
Green: used by both deep-blue based and IR-visible based detection algorithms
Blue: only used by deep-blue based detection algorithm
Brown: only used by IR-Visible based detection algorithm.
*: band is missing but using the corresponding band in the parentheses instead.
X: channel is missing, but not needed, and filled with “-999.9”
Sensors and Wavelengths

## Slide 6: EPS Aerosol Detection Algorithm Overview (1)
smoke
dust
clear
smog
Absorbing Aerosol Index
AAI = -100[1og10(R412/R440) – log10(R’412/R’440)]
Dust Smoke Discrimination Index
DSDI = -10[1og10(R412/R2250)
Input Reflectances:
Dust: 412, 440, 2250 nm
Smoke: 412, 440, 2250 nm
Spatial Variability Test: 412 nm
Turbid Water Test: 488 nm, 1.24 µm, 1.61 µm, 2.25 µm
Bright Pixel Test:1.24 µm, 2.25 µm
NDVI Test: 640 nm, 865 nm
Snow Test: 865 nm, 1.24 µm

## Slide 7: EPS Aerosol Detection Algorithm Overview (2)
Thick Dust
Thin Dust
Clear Sky
Thick Smoke
Thin Smoke
Clear Sky
Clouds
Algorithm takes advantage of spectrally varying absorption and scattering of dust, smoke, clouds, and surface
For illustration purpose, scenes with dust, smoke, clouds, and clear sky over Ocean were manually chosen

## Slide 8: Status of the EPS algorithm
Developed, tested, and implemented on Direct Broadcast data covering the CONUS. eIDEA displays the data.
  Download data and/or imagery in near real time
It is new. Not operational (24/7) yet globally for data coming into NOAA operations. Expected to be by November 2016
Reprocessed entire 2015 global data and other select time periods
NOAA Satellite Aerosol Product Workshop
September 13-14, 2016

## Slide 9: Dust Detection Product Improvements: Operational vs. EPS

## Slide 10
Ash Dust Smoke Sea Salt Undetermined None
Removed in EPS
Operational
EPS
MISR
June 2013
0.25o x 0.25o

## Slide 11: EPS: Himawari-8 AHI
NOAA Satellite Aerosol Product Workshop
September 13-14, 2016

## Slide 12: EPS: SNPP VIIRS
June 28, 2015
June 29, 2015
June 30, 2015
NOAA Satellite Aerosol Product Workshop
September 13-14, 2016

## Slide 13: Performance Metrics (VIIRS vs. CALIPSO): Operational vs. Reprocessed
Type | True positive | False positive | True negative | False Negative | Accuracy (%) | POCD (%) | POFD (%)
Dust | 2202 | 69 | 2397 | 375 | 91.1 | 85.3 | 3.1
Smoke | 117 | 98 | 4214 | 1 | 95.4 | 99.2 | 45.5
Land
Water
Type | True positive | False positive | True negative | False negative | Accuracy (%) | POCD (%) | POFD (%)
Dust | 297 | 11 | 139 | 10 | 95.4 | 96.4 | 3.3
Smoke | 107 | 85 | 2309 | 3 | 92.7 | 97.2 | 44.2
Chart: 
| Global | Ocean | Coastal | Land
M MEAN ACCY Dust | 0.58913 | 0.47902 | 0.60187 | 0.60126
M MEAN ACCY Smoke | 0.57661 | 0.56106 | 0.56826 | 0.58175
14-month Mean Accuracy
Operational
Reprocessed

## Slide 14
 | Pixel Quality Level |  |  |  | Applies to |  |  | 
Condition | Low | Medium | High | Not produced | Land |  | Water | 
 |  |  |  |  | smoke | dust | smoke | dust
Cloud contamination (corresponding tests in VCM/ECM shown cloudy or RM1>0.5) |  |  |  | x | x | x | x | x
Snow/ice (presence of snow/ice in ancillary snow/ice mask, or internal snow/ice test) |  |  |  | x | x | x | x | x
Cloud shadow | x |  |  |  | x | x | x | x
Cloud adjacency | x |  |  |  | x | x | x | x
fire spot | x |  |  |  | x |  |  | 
sun-glint | x |  |  |  |  |  | x | x
bright pixel | x |  |  |  |  | x |  | 
residual cloud (M1 STD>0.01) |  |  |  | x | x | x |  | 
residual cloud (M7 STD>0.005) |  |  |  | x |  |  | x | x
bad SDR |  |  |  | x | x | x | x | x
SZA>80° |  |  |  | x | x | x | x | x
SZA>65° and SZA<=80° | x |  |  |  |  |  |  | 
Turbid/shallow water |  |  |  | x |  |  | x | x
phytoplankton bloom |  |  |  | x |  |  | x | 
Overall Quality | Unless determined in above conditions, it is determined by the following paths |  |  |  |  |  |  | 
IR-visible algorithm path only | Determined by the average confidence value (between 0-1) for all tests. Confidence value for each test is calculated by how close the actual test value is to the threshold. If average confidence value < 0.33 then low quality is set If average confidence value > 0.66 then high quality is set Between 0.33 and 0.66 then medium quality is set |  |  |  | x | x | x | x
DAI-based algorithm path only | Determined by the average confidence value (0-1) for all tests. Confidence value for each test is calculated by how close the actual test value is to the threshold. ( Quality flags setting is the same as above) |  |  |  | x | x | x | x
Both algorithm path | Determined by ensemble confidence values from above two paths, i.e., ensemble confidence=average confidence(IR-visible path)+average confidence(DAI-based path) If ensemble confidence value < 0.33 then low quality is set If ensemble confidence value > 0.66 then high quality is set Between 0.33 and 0.66 then medium quality is set |  |  |  | x | x | x | x

## Slide 15: User Applications
eIDEA → accessed by operational air quality/weather forecasters (both AOD and aerosol detection are from EPS algorithms)
Smog blog (alg.umbc.edu/usaq)
Researchers
Exceptional events monitoring
Air quality modelers
Education and outreach (NOAA booth at AMS and AGU)
NOAA Satellite Aerosol Product Workshop
September 13-14, 2016

## Slide 16: Potential User Applications
HYSPLIT smoke forecast
µg/m3
NOAA Satellite Aerosol Product Workshop
September 13-14, 2016

## Slide 17: Acknowledgements
NOAA JPSS Program
NOAA GOES-R Program