## Slide 1: AerosolWatch: New NOAA Website for Near Real-Time ABI Aerosol Imagery
Amy K. Huff, Penn State University
Shobha Kondragunta, NOAA NESDIS
Hai Zhang, IMSG at NOAA
NOAA Satellite Aerosol Products Workshop September 26, 2017

## Slide 2: Open AerosolWatch Right Now!
AerosolWatch takes a few minutes to load
  Very high data volume!
You are going to work with site during activity. Get a head start by opening AerosolWatch right now, so it can load while I’m talking:
https://www.star.nesdis.noaa.gov/smcd/spb/aq/AerosolWatch/
For best results, open in Google Chrome!

## Slide 3: Summary of Key ABI Info
GOES-16 is in a geostationary orbit
  Very high temporal resolution!
Scan mode 3 (”flex mode”):
  15 min, full disk (North and South America)
  5 min, CONUS
  1 min, 2 mesoscale regions (selectable based on current hazards)
Very high data volume!!
GOES-16 currently in check-out position at 89 °W
  Will move to 75 °W in Nov and become GOES-East
  What are implications for US west coast data users?

## Slide 4: How Do We Make ABI Imagery Accessible?
VIIRS aerosol imagery is on eIDEA website
  Polar-orbiting satellite, so only one set of images per day
How to handle ABI imagery?
  High data volume (more images per day)
  Full disk and CONUS views
  More types of products
Result is new AerosolWatch website
  NRT ABI imagery animations for “today”
  Daily archive begins Sept 10, 2017
Currently, separate websites for JPSS (VIIRS) and GOES (ABI) products
  You tell us how to move forward

## Slide 5: Provisional ABI Products on AerosolWatch
Provisional maturity products can be used now:
  Synthetic RGB
    Band combination (made from multiple ABI bands)
    Like MODIS true color (RGB) but made with synthetic green band
    Looks like what you see with your eyes
  Dust RGB
    New product! Band combination
    Highlights blowing dust, which appears as magenta color
  Natural Color RGB
    New product! Band combination
    Highlights vegetation and cloud types; smoke appears turquoise
  Visible (Band 2 – red band – 0.6 mm)
    Similar to current GOES visible band (black/white/grey)

## Slide 6: b-Maturity ABI Products on AerosolWatch
b-maturity products are NOT recommended for use yet; they are available for information purposes:
  Aerosol Optical Depth (AOD)
    Similar to VIIRS AOT
    Quantitative measure of aerosols in atmosphere
  Smoke/Dust Mask
    Similar to VIIRS smoke/dust mask
    Highlights smoke (pink) and dust (yellow)
    Qualitative measure of aerosols in atmosphere
  Fires (Fire Radiative Power or FRP)
    Similar to VIIRS FRP
    Red hotspots indicate location of fires sensed by ABI
    Size of dots is a quantitative measure of FRP

## Slide 7: Data Characteristics on AerosolWatch
Latency: ~20 min (note typo in activity worksheet)
Temporal resolution: 15 min for full disk and CONUS
  Data start flowing at sunrise!
  Not max of 5 min for CONUS in order to make data volume manageable
Spatial resolution
  Full disk: all products 4 km
  CONUS 1 km:
    Synthetic RGB
    Natural color RGB
    Visible (red band)
  CONUS 2 km:
    Dust RGB
    AOD
    Smoke/dust mask
    Fires

## Slide 8: Aerosol Watch Homepage
Select ABI Layer
CONUS or Full Disk view
Zoom in/out
Animation controls
Open archive;
Time Stamp
Overlay state and national labels
Default is “today,” CONUS view, synthetic RGB

## Slide 9: Dust RGB with Labels Layer
Can only view one color imagery layer at a time
Legend for chosen layer(s)
“Eye” symbol indicates if layer is “on” or “off”

## Slide 10: Full Disk Synthetic RGB with AOD Overlay

## Slide 11: Some Things to Keep In Mind
No way currently to save images or animations on AerosolWatch
  NOAA will make animations available via ftp once GOES-16 is operational (Nov 2017)
No 48-hr forward aerosol trajectories on AerosolWatch
  We’re working on it
  Need to consider how to address huge data volume
As new data become available during day, AerosolWatch will NOT automatically update
  If you open AW in morning, for example, you will need to refresh periodically as new images become available every ~15 min

## Slide 12: Reminder: VIIRS Imagery on eIDEA
http://www.star.nesdis.noaa.gov/smcd/spb/aq/eidea/
main product overlay buttons
animations and external links

## Slide 13: VIIRS 48-Hour Forward Aerosol Trajectories
Trajectories give idea of transport of aerosol plumes
Areas of high AOT (>0.4) used as starting locations
Trajectories initialized at 50, 100, 150, and 200 mb above surface
  Trajectories run using NAM 12Z run output:
    Pink: near surface
    White: away from surface
  850 mb wind vectors (white)
  3-hr accumulated precipitation (yellow)
Magenta/pink lines indicate transport of smoke south into U.S., remaining near surface
Smoke transport from Ft McMurray fire May 6-7, 2016

## Slide 14: AerosolWatch Activity
Please break into groups of 2-3; at least one group member must have a laptop
Look at the ABI imagery on AerosolWatch, both CONUS and full disk
Use the “Case Study Worksheet” to guide your analysis
Answer questions on the “Case Study Questionnaire”
  Will help guide our discussion (~4:30 PM)
  And I’ll collect it so we can capture your feedback
If you have time, use the available ABI imagery from AerosolWatch and available VIIRS imagery from eIDEA and do a mock forecast for tomorrow