## Slide 1: Recent Impacts of Fire and Smoke on Air Quality Forecasting in the Mid-Atlantic
Bill Ryan
Penn State
Department of Meteorology
NOAA Satellite Aerosol Products Workshop
National Center for Weather and Climate Prediction
September 25-26, 2017

## Slide 2: This Must Be The New World
Emissions of O3 and PM2.5 precursors, primarily NOx and SOx, in the eastern US have been reduced dramatically over the past two decades.
These reductions in precursor emissions resulted in large decreases in ambient concentrations of both primary and secondary pollutants of interest to air quality forecasters.

## Slide 3: Mid-Atlantic Monitors Above Thresholds (Averages for 8-h >= 96 ppbv)
Chart: Number of Monitors Above Threshold
| 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0
>= 76 ppbv | 1293 | 1802 | 1183 | 1856 | 2525 | 2234 | 875 | 1704 | 2320 | 615 | 452 | 863 | 757 | 914 | 517 | 65 | 632 | 501 | 617 | 46 | 56 | 116 | 119
>= 96 ppbv | 149 | 408 | 82 | 378 | 335 | 442 | 156 | 269 | 524 | 143 | 25 | 53 | 46 | 44 | 30 | 4 | 43 | 33 | 26 | 0 | 0 | 1 | 1
>= 116 ppbv | 11 | 65 | 1 | 69 | 9 | 55 | 24 | 10 | 58 | 21 | 0 | 0 | 0 | 6 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1994-2002: 305 yr-1
2013-2016
0.5 yr-1
Notes: Figure 1. The number of monitors exceeding selected O3 mixing ratio thresholds in the mid-Atlantic coastal plain from 1994 to 2016. Number values are shown for exceedances of the 96 ppbv threshold.

## Slide 4: Shenandoah NP (Big Meadows) PM2.5 “Bad Air” Days
Chart: IMPROVE - SNP, Worst 20% Days
| 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0
Amm. Sulfate | 11.5 | 12.2 | 13.2 | 14.4 | 13 | 13.2 | 15.6 | 13.5 | 12.7 | 7.2 | 7 | 5.1 | 4.6 | 4.3 | 4.6 | 4.3 | 4.2
Total Mass | 18.4 | 18.2 | 19.2 | 21.6 | 18.8 | 19.2 | 20.3 | 19 | 19.1 | 12.7 | 12.3 | 9.1 | 8.6 | 8.6 | 8.6 | 8.6 | 9.9
~ 12 μgm-3
Notes: Figure 2. SNP surface PM2.5 observations at SNP via IMPROVE monitor observations.

## Slide 5: No Good Deed Goes Unpunished
As the “regional load” of O3 and fine particles has decreased, forecasting episodes of poor air quality has become more difficult.
The conceptual model of a “standard” poor air quality weather pattern is no longer reliable.
  In general, high frequency variations in metropolitan-scale peak O3 responds as much to meso-scale as synoptic scale effects.

## Slide 6: Hot Weather Is No Longer a Good Predictor of Poor Air Quality
Chart: Ratio of Days Above Threshold Given Tmax >= 90 F
| 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0
Ratio76 | 0.975 | 0.70588 | 0.80952 | 0.66667 | 1 | 0.90909 | 1 | 0.9 | 0.94737 | 0.95122 | 0.80952 | 0.8 | 0.77419 | 0.68 | 0.74074 | 0.6087 | 0.33333 | 0.54545 | 0.51515 | 0.5641 | 0.15 | 0.16 | 0.21622 | 0.15217
Ratio96 | 0.6 | 0.32353 | 0.45238 | 0 | 0.73684 | 0.45455 | 0.6129 | 0.4 | 0.63158 | 0.5122 | 0.14286 | 0.2 | 0.32258 | 0.28 | 0.22222 | 0.13043 | 0 | 0.036364 | 0.060606 | 0.051282 | 0 | 0 | 0.027027 | 0
Likelihood of exceeding 76 ppbv given Tmax ≥ 90°F.
Notes: Basic Statistics: Association of Tmax and Peak O3
PHL Metro Area, JJA, Domain Peak 8-h O3
r
r2
Best Linear Fit
2005-2007
0.77
0.60
(2.25 * Tmax) – 125.2
2010-2012
0.74
0.55
(1.74 * Tmax) – 87.5
2013-2016
0.55
0.30
(1.19 * Tmax) – 44.6
Table 2. Correlation with Tmax (JJA, peak domain 8-h ozone) in the PHL metro forecast area.

## Slide 7: Tmax and Local Persistenc Are Much Weaker Predictors of Peak O3
Chart: Variance (r2) in Peak 8-h Ozone
| Tmax | Persistence
2004-2012 | 0.58 | 0.36
2013-2016 | 0.3 | 0.18

## Slide 8: Transport Patterns: Meso-scale Recirculation?
Chart: PHL Metro, 96th%ile Ozone Days, Back Trajectory Length (1000 m, 24 h)
| 1999-2001 | 2005-2007 | 2010-2012 | 2013-2016
Mean | 516.2941 | 489.5263 | 510.3 | 333.2812
Median | 474 | 451 | 558 | 270.5
2005-2007
2013-2015

## Slide 9: Numerical AQ Forecast Models Tend To Under-Predict on the “Worst” O3 Days
Shown at left, observations and numerical model forecasts for Philadelphia metropolitan area peak O3, 2014-2016.
Red bar demarcates observed peak O3 ≥ 80 ppbv.
Strongest events are routinely under-predicted.

## Slide 10: Worst Air Quality Days Now Rare
In the PHL metro area, days with peak 8-hour O3 ≥ 80 ppbv have become rare beginning in 2014.
  Also true of the coastal mid-Atlantic.
In total, for the period 2015-2017, there were a total of 19 days ≥ 80 ppbv with 70 monitors reaching that threshold – approximately 3 monitors per event.

## Slide 11: A Closer Look Shows That Truly Widespread High O3 is Even Rarer
Chart: Case Number
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0
Monitors | 12 | 1 | 12 | 9 | 6 | 2 | 1 | 1 | 2 | 4 | 1 | 1 | 1 | 1 | 2 | 9 | 2 | 2 | 1
60% of the monitors exceeding 80 ppbv
occurred on only 4 days!

## Slide 12: The Four Very Bad Days
It appears that remnant wildfire smoke is a factor in all of these widespread high O3 days.

## Slide 13: Mother of All Mid-Atlantic Smoke Events (July, 2002)

## Slide 14: MODIS AOD (Aqua) June 10 (left) and June 11 (right)

## Slide 15: UMBC ELF Aerosol Backscatter (left) and AIRNow O3 Map (right)
Figure courtesy of UMBC (Smog Blog), data from Elastic Lidar Facility (ELF).

## Slide 16: Regional O3 Event May 25-26, 2016

## Slide 17: VIIRS Image, May 22 (left) and Back Trajectory for May 24 (right)

## Slide 18: VIIRS Images for May 24 (left) and May 25 (right)

## Slide 19: VIIRS Image with Smoke Mask May 16 (left) and May 17 (right)

## Slide 20: AirNow O3 Maps May 17, 2017 (left) and May 18 (right)

## Slide 21: VIIRS Image with Smoke Mask July 19, 2016 (left), July 20 (right)

## Slide 22: Back Trajectory for July 22 (left) and AirNow O3 (right)

## Slide 23: Comments (1 of 2)
The frequency of widespread O3 events in the mid-Atlantic have been significantly reduced – nearly eliminated – by emissions reductions on the local and regional scale.
The “very bad air” days that remain appear to be enhanced by wildfire smokes emissions.

## Slide 24: Comments (2)
The extent of this enhancement by wildfire smoke remains uncertain.
In the most recent cases there has been no significant signature in total mass PM2.5.