## Slide 1: SNPP VIIRS Dust and Smoke Products
Shobha Kondragunta1 and Pubu Ciren2
1NOAA/NESDIS/STAR 2IMSG@NOAA
NOAA Satellite Air Quality Proving Ground Workshop
September 9, 2015

## Slide 2: SNPP VIIRS Suspended Matter (SM)
Output for each pixel (~750 m)
  SM type flag (1 – yes; 0 – no)
  Volcanic ash flag – passed on from VIIRS cloud mask algorithm
  Dust flag
  Smoke flag
  Smoke concentration (right now fill values)
  No aerosol
  Unknown aerosol
  Clear sky
Quality flags
  Low
  Medium
  High

## Slide 3
Detection not performed for the following conditions:
  Clouds: screened by using R412 nm and cloud mask
  Residual clouds
    Over water: screened by 860 nm spatial variability test
    Over land: screened by using 412 nm spatial variability test
  Bright surfaces: normalized difference index of 1.24 and 2.25 µm
  Turbid water: screened using 746 nm and 1.24 µm
  Sunglint
  Snow/ice
  fires
DAI = -100*[log10(R412nm/R445nm)-log10(R’412nm/R’445nm)]
NDAI = -10*[log10(R412nm/R2250nm)]
Dust Aerosol Index (DAI)
R’ -- reflectance from Rayleigh scattering

## Slide 4: Product Accuracy
Chart: Dust
| Accuracy | Probability of Correct Typing | False Alarm Ratio
Land | 84.4 | 80 | 1.6
Water | 95.4 | 96.4 | 3.3
Chart: Smoke
| Accuracy | Probability of Correct Typing | False Alarm Ratio
Land | 99.1 | 96.7 | 34.1
Water | 94 | 97.5 | 45.7
  Two years of SNPP VIIRS dust and smoke detection product validated against CALIPSO

## Slide 5: Product Accuracy
Dust
Smoke
Two years of VIIRS smoke/dust vs. AERONET aerosol classification based on Angstrom Exponent

## Slide 6: Transatlantic dust transport
Year of 2014
May 10, 2015

## Slide 7
May 10, 2015
Sunglint region

## Slide 8
May 10, 2015

## Slide 9: Smoke Transport June 8 to July 15, 2015

## Slide 10
12 Aug
13 Aug
14 Aug
15 Aug
16 Aug
17 Aug
12 Aug
13 Aug
14 Aug
15 Aug
16 Aug
17 Aug

## Slide 11
12 Aug
13 Aug
14 Aug
15 Aug
16 Aug
17 Aug
OMPS
VIIRS

## Slide 12
June 10, 2015
OMPS
VIIRS

## Slide 13
August 9, 2015
Dry lake beds flagged as smoke
Some bright surfaces get flagged as smoke

## Slide 14
M5: 672 nm
M8: 1240 nm

## Slide 15
July 9, 2015
Smoke mis-identified as cirrus flag in VCM

## Slide 16
With cirrus flag turned off

## Slide 17
Smoke plume

## Slide 18
With cirrus flag turned off

## Slide 20
Smoke near clouds assigned “low quality” using a standard deviation test:
StdDev_M1 > 0.01

## Slide 21: Backup Slides

## Slide 22: Validation Strategy
Dust/smoke detection algorithm run on VIIRS data for the entire year of 2013 and 2014.
  VIIRS smoke/dust detection matchup with AERONET Observations
  VIIRS smoke and dust detection matchups with CALIPSO VFM
Derive performance metrics
  Accuracy
  Probability of Correct Detection (POCD)
  Probability of False Detection (POFD)
 | Yes | No
Yes | A | B
No | C | D
VIIRS
TRUTH DATA
POCD = A/(A+C)
POFD = B/(A+B)
Accuracy* = (A+D)/(A+B+C+D)

## Slide 23: VIIRS vs. CALIPSO
Global Granules for the year of 2013
Type | True positive | False positive | True negative | False Negative | Accuracy (%) | POCD (%) | FAR (%)
DUST | 10669 | 170 | 5676 | 2840 | 84.4 | 80.0 | 1.6
SMOKE | 307 | 159 | 19534 | 14 | 99.1 | 96.7 | 34.1
Land
Water
Type | True positive | False positive | True negative | False negative | Accuracy (%) | POCD (%) | FAR (%)
DUST | 297 | 11 | 139 | 10 | 95.4 | 96.4 | 3.3
SMOKE | 601 | 507 | 7605 | 15 | 94.0 | 97.5 | 45.7
Year of 2013 and 2014

## Slide 24
Stations |  | True positive | False positive | True negative | False negative | Accuracy | POCD | POFD
Darkar | 2013 | 63 | 1 | 106 | 10 | 93.9 | 86.3 | 0.2
 | 2014 | 74 | 3 | 45 | 10 | 90.1 | 88.1 | 0.4
Solar_Village | 2013 | 81 | 26 | 59 | 30 | 71.4 | 73.0 | 24.3
 | 2014 | 11 | 4 | 65 | 5 | 89.4 | 68.8 | 26.7
Capo_Verde | 2013 | 44 | 0 | 56 | 3 | 97.1 | 93.6 | 0.0
 | 2014 | 53 | 1 | 17 | 1 | 97.2 | 98.1 | 0.2
Over 440 AERONET stations | Accuracy | POCD | POFD
Year of 2013 and 2014 | 98.5 | 84.6 | 14.7
VIIRS vs. AERONET (DUST)

## Slide 25
Stations (Biomass –burning) | True positive | False positive | True negative | False negative | Accuracy | POCD | POFD
Alta_Floresta | 10 | 0 | 178 | 0 | 100.0 | 100.0 | 0.0
Bonanza_Creek | 1 | 0 | 48 | 0 | 100.0 | 100 | 0.0
Jabiru | 1 | 0 | 313 | 0 | 100.0 | 100.0 | 0.0
Moscow_MSU_MO | 16 | 2 | 92 | 1 | 97.2 | 94.1 | 11.0
Tomsk_22 | 17 | 1 | 83 | 0 | 99.0 | 100.0 | 5.0
Yakutsk | 22 | 1 | 88 | 1 | 98.2 | 95.6 | 4.3
Over 401 AERONET stations | Accuracy | POCD | POFD
Year of 2013 and 2014 | 97.5 | 91.6 | 18.5
VIIRS vs. AERONET (Smoke)

## Slide 26
VIIRS vs. AERONET (dust)

## Slide 27
VIIRS vs. AERONET (smoke)

## Slide 28: Near-real time run of JPSS SM algorithm on S-NPP VIIRS DB data
JPSS RR SM algorithm has been Implemented by using near-real time S-NPP VIIRS DB data over both CONUS and OCONUS
It provides daily monitoring of smoke/dust event OVER CONUS and Alaska

## Slide 29: Summary
JPSS RR Suspended Matter algorithm is simple, fast, and easy to be implemented operationally.
Validation results indicated that Accuracy and POCD for dust and smoke detection can be as high as 90% and 80 %, respectively.
Additional investigation of data artifacts (false detections) is required to enhance product accuracy.