## Slide 1: Using VIIRS Aerosol Products in an Operational Environment
Hai Zhang1, Amy Huff2, , Shobha Kondragunta3 Hongqing Liu1, Pubu Ciren1
IMSG at NOAA
Pennsylvania State University
NOAA NESDIS
NOAA Satellite Air Quality Proving Ground Annual Advisory Group Workshop 2015
9/9/2015

## Slide 2: Outline
Introduction to IDEA
Demo of IDEA for VIIRS
Issues users should be aware of

## Slide 3: IDEA: Infusing satellite Data into Environmental Applications
Provide near-real-time satellite aerosol information and analysis over the United States to the operational air quality community
Satellite data
  MODIS Terra, Aqua, VIIRS, GASP East, GASP West
    AOD (aerosol optical depth) or AOT (aerosol optical thickness)
    RGB images (MODIS, VIIRS)
Other data for analysis
  Meteorological data: wind, precipitation
  In-situ PM2.5
  OMI Aerosol Index (AI)
  WF_ABBA (Wild Fire Automated Biomass Burning Algorithm), fire hotspots
  Developed by NASA for MODIS and transitioned to NOAA. NOAA enhanced IDEA to include GOES-E, GOES-W, OMI, VIIRS and surface PM2.5 estimation

## Slide 4
IDEA Data flow diagram
MODIS data processing L1B, aerosol products
EPA AIRNow PM2.5
NOAA
Meteorological data
NOAA
WF_ABBA
Data processing, forward trajectories, composite plots, etc
IDEA Website
MODIS Terra and Aqua
GOES
East
and West
GOES data processing
GASP Aerosol product
Local computer at NOAA
VIIRS L1B, cloud mask data
Generate VIIRS aerosol product locally (STAR research version)
http://www.star.nesdis.noaa.gov/smcd/spb/aq/
VIIRS

## Slide 5: IDEA web page http://www.star.nesdis.noaa.gov/smcd/spb/aq/
Click tabs to select satellite
Click panels to select product

## Slide 6: Products on IDEA
Satellite RGB and AOD images, VIIRS smoke/dust mask, fire hotspots
48-hour forward trajectories
3-day composite history of AOD, wind, in-situ PM2.5, and fire hotspots
Daily PM2.5 estimates from MODIS AOD
AOD-PM2.5 correlation, Estimated PM2.5 vs in-situ PM2.5 correlation and RMSE maps
Time series, scatter plots, histogram, etc for AOD, estimated and in-situ PM2.5 at PM2.5 stations

## Slide 7: New Updates on IDEA
Interactive google map for VIIRS since 1/6/2014
VIIRS AOT products EDR (6 km), IP (750 m) and quality selection
VIIRS smoke/dust mask images
VIIRS fire hotspots

## Slide 8: Main page of VIIRS CONUS
Click here to get to this page
Click each image to get to the individual product

## Slide 9
VIIRS CONUS imagery on google map

## Slide 10
VIIRS CONUS imagery on google map

## Slide 11
VIIRS CONUS imagery on google map
These two buttons will appear when IP AOT is selected

## Slide 12
VIIRS CONUS forward trajectory

## Slide 13
VIIRS CONUS forward trajectory
AOD (red-blue)
850 mb winds (white arrows)
Precipitation (yellow)
Trajectories from high AOD regions (pink-white):
  Dark pink – close to the surface
  White – high above surface
Verification plot is linked to the AOD plot two days later
Initiated at locations with AOD > 0.4, 50mb, 100mb, 150mb, and 200 mb above the surface
48 hour trajectories

## Slide 14: VIIRS CONUS forward trajectory
AOD (red-blue)
850 mb winds (white arrows)
Precipitation (yellow)
Trajectories from high AOD regions (pink-white):
  Dark pink – close to the surface
  White – high above surface
Verification plot is linked to the AOD plot two days later
Initiated at locations with AOD > 0.4, 50mb, 100mb, 150mb, and 200 mb above the surface
48 hour trajectories

## Slide 15: Forward trajectory initiated from other satellites’ aerosol data
MODIS Terra, GASP, GASP-West: Same initialization condition as VIIRS, i.e. initiated at locations with AOD > 0.4, 50mb, 100mb, 150mb, and 200 mb above the surface)
MODIS Aqua AOD and OMI AI (aerosol index)
  If AI is higher than 2.0, we will initialize the trajectories at 300mb above surface
  Otherwise, same as above

## Slide 16
VIIRS CONUS imagery (original version)

## Slide 17
VIIRS CONUS imagery (original version)

## Slide 18
VIIRS OCONUS (Alaska) imagery

## Slide 19
VIIRS OCONUS (Alaska) imagery

## Slide 20: Granule Overlap region
VIIRS covers some regions twice per day during sun-lit time with time difference of about 1.5 hours
On IDEA in the overlapping region
  We display RGB of the latest overpass
  We display AOD and dust/smoke mask of the latest overpass if there are retrievals. Otherwise, we show AOD and dust/smoke mask from the previous overpass.
  This can improve aerosol data coverage, but may lead to some confusions.

## Slide 21
Granule overlap example 20150418
Second overpass
AOT & smoke/dust mask
AOT & smoke/dust mask
First overpass

## Slide 22
Choice I
show bottom granule AOT and smoke/dusk mask if top granule does not have retrievals
Better data coverage
Inconsistency
currently adopted on IDEA
Choice II
only show latest AOT and smoke/dusk mask
No inconsistency
less data coverage
Currently not used on IDEA
Granule overlap example 20150418
When we plot the two overpass on the same image, we can have to choices:

## Slide 23
Granule Overlap – another example 20150831
Looks like some AOT retrievals are over cloudy region. But the AOT retrievals are from the earlier granules when those pixels are cloud free.

## Slide 24
Granule overlap is also in MODIS AOD images

## Slide 25: VIIRS IP AOT high *
VIIRS IP AOT high * quality include high quality AOT pixels and degraded AOT flagged as “soil dominated” and “cirrus” pixels
Improve data coverage over western US for qualitative use

## Slide 26: Summary
VIIRS imagery products on IDEA
  RGB
  AOT with different qualities
  Smoke cloud mask
  Fire hotspots
  Forward trajectory
CONUS and OCONUS regions
Issues
  Granule overlap
  VIIRS IP AOT high *

## Slide 27: Acknowledgements
Liam Gumley and Kathy Strabala (University of Wisconsin Madison)
  Direct broadcast VIIRS data over CONUS
Scott Macfarlane (Univ. of Alaska)
  Direct broadcast VIIRS data over Alaska