## Slide 1: VIIRS Suspended Matter and Dust Aerosol Index Product
Shobha Kondragunta1, Pubu Ciren1,2 and Ho-Chun Huang1,3
1NOAA/NESDIS
2IMSG
3UMD-CICS

## Slide 2: Suspended Matter
Suspended matter consists of particles such as sand, dust, smoke,
volcanic ash, and urban/industrial particulate matter. It can damage
many different systems. For example, aircraft flying through these
materials can suffer damage to cockpit canopies or windscreens.
Additionally, aircraft engines suffer extremely high wear in the presence
of suspended matter, leading to increased sustainment or engine failure.
Volcanic ash plumes are a threat to military and civil aviation. DOC
participates in a civil aviation warning system for volcanic ash hazards
by monitoring these plumes in satellite imagery. DOC also monitors
smoke from large scale fire events to provide information to the relevant
agencies and the public. Suspended matter is detected in a pixel when
Aerosol Optical Thickness (AOT) is greater than 0.15 but for the quality
of the suspended matter type (dust/sand, smoke, volcanic ash, sea salt) to
be “high”, the AOTs should be at least 0.5 or higher.
From L1RD supplement

## Slide 3: JPSS L1RD Supplement Requirements
Product | Threshold | Objective | Notes
SM | Dust, smoke, volcanic ash | Dust, smoke, volcanic ash, sea salt | 
Smoke plume | 0 to 150 µg/m3 | 0 to 200 µg/m3 | 
Accuracy |  |  | 
SM | 80% |  | 
Smoke | 70% |  | 
Dust | 80% |  | 
Ash | 60% |  | Dust can be mis-identified as ash
Mixed Aerosol |  | 80% | Report not only dominant aerosol but other aerosol components as well

## Slide 4: VIIRS SM Algorithm Overview
Smoke
Fine Mode Weight (FMW)
FMW < 0.2
AOT < 0.3
AOT
0.2 ≤ FMW < 0.5
AOT ≥ 0.3
FMW ≥ 0.5
Dust
Sea Salt
Undetermined
AOT Model Selection
Dust Model
Any other Model
Dust
Smoke
Ocean
Land
Dependence on Fine Mode Weight (FMW)
From SM ATBD prepared by NGAS, dated 3/17/2010
Tuned out due to too many false positives as of 11/2/2012
VCM
Ash

## Slide 5: Heavy Aerosol Flag vs. SM
VCM attempts to identify the presence of heavy aerosol flag for scenes that are classified as “confidently/probably cloudy” and passes that information to aerosol algorithm.
  Aerosol algorithm uses it to reset “confidently/probably cloudy” pixels as clear sky to attempt AOT/Angstrom Exponent/SM retrieval.
  If heavy aerosols (dust and smoke) are indeed present, AOT up to 2.0 is retrieved. AOTs higher than 2.0 are flagged as “out of range”.
  If the pixels are indeed cloudy, AOTs will be high and likely out of range as well.
SM algorithm does not rely on heavy aerosol information from VCM except for “volcanic ash”.
  But, VCM tuned out all volcanic ash testing as of November 2, 2012

## Slide 6: SM Product Validation
Qualitative comparison of monthly global maps of VIIRS SM (dominant aerosol type), dust fraction, and smoke fraction to CALIPSO and MISR products
    CALIPSO: 5o x 5o
      Coarser grid for CALIPSO is used to obtain a good sample size.
  MISR: 0.25o x 0.25o
  VIIRS: 0.25o x 0.25o
Direct matchups of CALIPSO and VIIRS SM to compute accuracy, probability of detection, and false alarm ratio.

## Slide 7: June 2013 VIIRS vs. MISR

## Slide 8: June 2013 VIIRS vs. CALIPSO

## Slide 9: June 2013 VIIRS vs. MISR

## Slide 10
Time difference: ±2 minutes
Spatially , VIIRS pixels within ± 375m of the middle CALIPSO profile are selected.
Middle three profiles are used to determine aerosol type in the column
  All three profiles need to be cloud-free;
  Dominant aerosol type is determined through the calculation of dust (or smoke) fraction ( i.e., no of dust (or smoke) layers divided by the no. of aerosol layers from surface to 12km.
VIIRS SM data are filtered for high quality.
375m
330m
5km
CALIPSO
VIIRS pixels
CALIPSO – VIIRS Matchups
True Positive (TP): VIIRS and CALIPSO say dust
True Negative(TN): VIIRS and CALIPSO say no dust
False Negative(FN): VIIRS says no dust but CALIPSO says dust
False Positive(FP): VIIRS says dust when CALIPSO says no dust
POD = TP/(TP+FN)
Accuracy = (TP+TN)/(TP+TN+FP+FN)
FAR = FP/(FP+TP)

## Slide 11
VIIRS vs. CALIPSO Matchup
January 31, 2013
Accuracy | 2.3%
Probability of Detection | 0.0%

## Slide 12: Analysis of VIIRS FMW
MODIS shows lower FMW near the dust source regions. This feature is missing in VIIRS due to which SM algorithm misses dust detection.

## Slide 13: Dust Aerosol Index (DAI) Algorithm
Developed for MODIS
  Ciren and Kondragunta, JGR, in review, 2013
Algorithm adapted for VIIRS
  Only VIIRS dust results shown in this presentation. Figures related to algorithm are from MODIS and are used to illustrate the algorithm physics
  MODIS and VIIRS bands are similar but not identical

## Slide 14: 6S Radiative Transfer Simulations
6S Simulations:
MODIS C5 dust aerosol model used
Desert, vegetation, ocean BRDF with easterly wind speed of 6 m/s are used to represent surfaces in 6S
Finding:
DUST reduces the contrast between 412nm and 440 nm as a result of increasing absorption by dust with decreasing wavelength
R412nm/R440nm

## Slide 15: MODIS Observations

## Slide 16: MODIS Observations
Smoke:
Has the same effect as dust in terms of the reduction in the contrast of 412 nm to 440 nm
But, smoke particles are smaller than dust. Reflectance at 2.13 µm can be used to separate dust from non-dust aerosols.
Ref(2130nm)

## Slide 17: Dust Aerosol Index
DAI = 100*[log10(R412nm/R445nm)-log10(R’412nm/R’445nm)]
NDAI = -10*[log10(R412nm/R2.25µm)]
Clouds over water are screened using 0.86 µm spatial variability test. Over land, clouds are screened by 1.38 µm test for cirrus and 412 nm spatial variability test
Bright desert surfaces are screened for by bright pixel index (normalized difference of 1.24 µm and 2.25 µm)
Sunglint, snow/ice, fire hot spots are also screened based on different tests (geometry, spectral etc.)
DAI and NDAI are computed for pixels that pass these tests:
  Water: DAI ≥ 4 and NDAI ≥ -10
  Land: DAI ≥ 12 and NDAI ≥ 0
6S Simulations for MODIS bands

## Slide 18: Dust Aerosol Index
DAI = 100*[log10(R412nm/R445nm)-log10(R’412nm/R’445nm)]
NDAI = -10*[log10(R412nm/R2.25um)]
Clouds over water are screened using 0.86 um spatial variability test. Over land, clouds are screened by 1.38 um test for cirrus and 412 nm spatial variability test
Bright desert surfaces are screened for by bright pixel index (normalized difference of 1.24 um and 2.25 um)
Sunglint, snow/ice, fire hot spots are also screened based on different tests (geometry, spectral etc.)
DAI and NDAI are computed for pixels that pass these tests:
  Water: DAI ≥ 4 and NDAI ≥ -10
  Land: DAI ≥ 12 and NDAI ≥ 0
MODIS observations

## Slide 19: Dust Aerosol Index
03/10/2013
OMPS Aerosol Index
Haze
Dust
VIIRS Dust Aerosol Index

## Slide 20: June 2013 VIIRS vs. MISR
Operational

## Slide 21: June 2013 VIIRS vs. MISR
Dust Frequency Map from DAI algorithm for June 2013
DAI

## Slide 22
VIIRS vs. CALIPSO Matchup
January 31, 2013
Accuracy | 2.3%
Probability of Detection | 0.0%
SM Operational

## Slide 23
VIIRS vs. CALIPSO Matchup
January 31, 2013
Accuracy | 83%
Probability of Detection | 85%
SM DAI

## Slide 24: Some Key Remarks on SM
SM is not a legacy NASA MODIS product
VIIRS SM algorithm relies on AOT and other internal parameters (not validated) to identify and type SM.
  Aerosol FMW over ocean
  Aerosol model over land
SM product very difficult to evaluate and validate
  Reliance on other satellite (CALIPSO and MISR) data.
  In situ (IMPROVE network) data are available but with a 1 to 2 yr latency.
  AERONET Angstrom Exponent based classification can be used but not really “truth” like the AERONET AOT product is.
The VIIRS SM product is not recommended for use in any applications. DAI algorithm will be implemented in the future.

## Slide 25: Acknowledgements
National Weather Service for partial funding to develop DAI algorithm for MODIS (FY08-FY13)
NASA for MODIS Level 1 radiances, MISR and CALIPSO retrieved products
JPSS program