## Slide 1: Estimating Surface PM2.5 Concentrations using Satellite AOD
Sundar A. Christopher
The University of Alabama in Huntsville
sundar@nsstc.uah.edu
VIIRS Aerosol Science and Operational Users Workshop November 21-22, 2013
Hoff, R., S.A. Christopher, Remote Sensing of Particulate Matter Air Pollution from Space : Have we reached the promised land?, J. Air & Waste Management Association, 59:642-675, 2009.

## Slide 2: What is PM2.5?
Particles < 2.5µm in diameter – ‘Fine Particles’
All types of combustion – examples : motor vehicles, power plants, forest/agricultural burning,

## Slide 3: Why study PM2.5?
Premature Mortality Risk
1996-1998 Fine Mass
Health studies show link between increased PM2.5 mass and premature mortality.
10 µgm-3 increase in PM was associated with 8% to 18% increases in mortality risk [Pope et al., 2003].
Huntsville
Alabama
Paciorek/ Hu/Al-Hamdan

## Slide 4
U.S. Air Quality Guidelines
Sensitive groups should avoid all physical activity outdoors; everyone else should avoid prolonged or heavy exertion
Sensitive groups should avoid prolonged or heavy exertion; everyone else should reduce prolonged or heavy exertion
Sensitive groups should reduce prolonged or heavy exertion
Unusually sensitive people should consider reducing prolonged or heavy exertion
None
Cautionary Statements
201-300
151-200
101-150
51-100
0-50
Index
Values
PM10
(ug/m3)
PM2.5
(ug/m3)
Category
355-424
255-354
155-254
55-154
0-54
150.5-250.4
65.5-150.4
40.5-65.4
15.5-40.4
0-15.4
Good
Very Unhealthy
Unhealthy
Unhealthy for Sensitive Groups
Moderate
NAAQS: 35 mg/m3 (24 h), 15 mg/m3 (annual)

## Slide 5: WHO - Guidelines
 | 24-Hour Av PM2.5 (μgm-3) | Basis for the selected level | Annual Average PM2.5 (μg m-3) | Basis for the selected level
Interim Target-1 (IT-1) | 75 | Based on published risk coefficients from multi-centre studies and meta-analyses (~ 5% increase of short-term mortality over the AQG value). | 35 | These levels are associated with about a 15% higher long-term mortality risk relative to the AQG level.
Interim Target-2 (IT-2) | 50 | Based on published risk coefficients from multi-centre studies and meta-analyses (about 2.5% increase of short-term mortality over the AQG value). | 25 | In addition to other health benefits, these levels lower the risk of premature mortality by approximately 6% [2–11%] relative to the IT-1 level.
Interim Target-3 (IT-3) | 37.5 | Based on published risk coefficients from multi-centre stud­ies and meta-analyses (about 1.2% increase in short-term mortality over the AQG value). | 15 | In addition to other health benefits, these levels reduce the mortality risk by approximately 6% [2-11%] relative to the IT-2 level.
Air Quality Guideline (AQG) | 25 | Based on the relationship between 24-hour and annual PM2.5 levels. | 10 | These are the lowest levels at which total, cardiopul­monary and lung cancer mortality have been shown to increase with more than 95% confidence in response to long-term exposure to PM2.5
NAAQS: 35 mg/m3 (24 h), 15 mg/m3 (annual)

## Slide 6: Surface PM2.5 mass monitors
1500
3-8
4-9
1-5
20-30
0-3
5-10
1-5
Number of Ground measurements are sparse and inadequate for monitoring global PM2.5 mass concentrations – especially outside the United States

## Slide 7: Satellite Remote Sensing
Satellites remote sensing is the only viable method for monitoring global particulate matter air pollution
CLOUDS
HAZE
SNOW
GLINT
SMOKE
GLINT
Engel-Cox

## Slide 8: VIIRS Example
Aerosol
Alabama
Birmingham

## Slide 9: But what do satellites measure?
Need surface PM2.5
Have column AOD
AOD is related to PM2.5 but need ancillary information
Satellite measured radiances
are converted to columnar
Aerosol Optical Thickness/Depth

## Slide 10: Satellite and ground-based data
Both Level 1 RGB imagery and level 2 aerosol product information is useful
Christopher, S.A., P. Gupta, U. Nair, T.A. Jones, S. Kondragunta, Y. Wu, J. Hand, X. Zhang, Satellite Remote Sensing and Mesoscale Modeling of the 2007 Florida/Georgia Fires, IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing (JSTARS-2009-00020), 26, 1-13, 2009

## Slide 11
0.0 0.2 0.4 0.6 0.8 1.0 0 10 20 30 40 50 60 70 0 15.5 40.5 65.5 150.5
Aerosol Optical Depth Cloud Optical Thickness PM2.5 (ug/m3)
Sept 9
Sept 10
Sept 11
Sept 12
No EPA sites
MODIS fills in
Notes: The IDEA project
Training (EPA, National Air Quality Conference, AWMA, United Nations)

## Slide 12: Correlating PM2.5 and AOD
For the easy (relatively) cases if there is a PM-AOD relationship (linear in this case) use AOD to estimate PM2.5
Wang and Christopher, 2003
Hourly, R= 0.7;Daily, R >0.9
Wang, J., and S. A. Christopher, Intercomparison between satellite-derived aerosol optical thickness and PM2.5 mass: Implications for air quality studies, Geophys. Res. Lett., 30(21), 2095, doi:10.1029/2003GL018174, 2003

## Slide 13: Creating AQI maps
Every pixel that is not cloud covered has an AQI value

## Slide 14: Uncertainties
Even though clouds prevent AOD retrievals ~50% of the time, difference between ALL
PM2.5 from ground and PM2.5 during time of satellite overpass is < 2ugm-3 for
seasonal and yearly averages (Christopher and Gupta, 2009).
Linear Correlation Coefficient
PM2.5 /AOD varies across studies due to different assumptions.
Uncertainty
Notes: Reasons include
Surface reflectance is higher in the West than the East
Predominantly sulfate type of aerosols in the East when compared to Nitrate type of aerosols in the West
Different meteorology and PBL heights

## Slide 15: Beyond the linear correlation
Van Donkelaar, et al 2006
PBL, RH are necessary to estimate PM2.5 from columnar satellite retrievals. Correlations increase from 0.3 to 0.7.
Aircraft studies also show that normalizing AOD with PBL height significantly improves AOD-PM2.5 relationship (Al-Saadi)
Predicted PM2.5
Observed PM2.5
Liu et al (2005)

## Slide 16: Progress
PM2.5=α+ α1*AOT+ α2*TMP+ α3*HPBL+ α3*WS+ α4*RH
PM2.5 Estimation from Satellite Observations (MODIS, MISR, GOES, POLDER)
THREE
Dozen +
Few
TWO?
AOT
PM2.5
Y=mX + c
MVM
Terra
2000
2003
2009
2005
Critical
Review
BAMS
Review
MODIS
MISR
2006
Global
Lidar
2008
GOES
POLDER
Fraser&
Kaufman
1984
Neural Networks
Multi-variate methods
Aqua
2002
2007
SeaWifs
2004
Two variate methods
1st
paper
2013
Epidemiology
VIIRS
Global Estimates

## Slide 17: VIIRS Examples
June 23, 2013
June 26, 2013
June 29, 2013

## Slide 18: Summary
Satellite data continue to be useful to monitor air pollution
With ancillary data sets, satellite AOD can be used to estimate PM2.5 concentrations across the earth. Especially useful where no ground monitors are available
Awareness in other communities (e.g. epidemiology) continues to increase